Toolkit Doc11 Head Pan Skins
April 30, 2010

---
Head Pan Tilt Right + Left R/R
Head Pan-tilt Right – 3181 or
Head Pan-tilt Left – 3183, Removal
  - Tilt the Head forward.
  - Using the 4mm bit with the T-handle driver, remove 2 screws. 3063-14 (Fig 1,2)
  - Grab the front lower corner of the cover and pull out gently until the snap releases. (Fig 3,4)
Fig 1
Fig 4
  - For the Right side move the cover slightly to the rear and up to clear the Aluminum boss. (Fig 5)
  - Then pull the cover out to remove.
Head Pan-tilt Right or Head Pan-tilt Left, Install
  - First slip the rear of the cover over the Aluminum boss. (Fig 6)
  - Push the center of the cover until the snap engages.
  - Using Loctite 248, install the screws and torque to 1.58Nm using the Large torque driver.
Fig 5
Fig 2
Fig 6
Fig 3

---
Head Collar R/R
Head Collar, Removal - 3183
  - Remove the Top Front Panel.
  - Tilt the Head completely forward, and using the 3mm bit with the T-handle driver, remove the screw. (Fig 1)
  - Tilt the Head completely backwards. Pulling firmly on the bottom of the Panel, releasing the 2 snaps. (Fig 2)
  - With the Panel bottom pulled out about 3cm, rotate the Panel downward to clear the bottom of the Faceplate, then pull out. (Fig 3)
Faceplate
Head Collar, Install
  - Reverse the removal procedures.
  - Push the center of the cover until the snaps engage.
  - Using Loctite 248, install the screw and torque to 1.36Nm using the Large torque driver.

---
Head Pan Rear R/R
Head Pan Rear, Removal - 2451
  - Using the 3mm bit with the T-handle driver, remove the 4 screws. (Fig 1)
  - Lift the Panel straight up and off. (Fig 2)
Head Pan Rear, Install
  - Reverse the removal procedure.
  - Using Loctite 248, install the 4 screws and torque to 1.36Nm using the Large torque driver.