Toolkit Doc15 Fan Filter
May 5, 2010

---
Fan filter R/R
Plate, Install
  - Reverse the removal procedure.
  - Using Loctite 248, install the 4 screws and torque to 1.58Nm using the Large torque driver. (Fig 3)
Fan Filter – 2802, Plate – 2781, Removal
  - Using the 2.5mm bit with the T-handle driver, remove 4 screw. 3064-06 (Fig 1)
  - Clean the filter by blowing the dust out or washing it with soap and water. Make sure it is dry before installing.
  - To expedite installation, turn on the robot so that the fan is running. The suction will hold the filter in place. Make sure it is centered.
    (Fig 2)
Fig 1
Fig 3
Fig 2