PR2 GPU Computer Configuration
1/11/2011
PR2 GPU Computer Configuration

Overview

This document contains instructions for computer configuration of a PR2 with an NVIDIA Quadro 600 GPU installed into c2. Read this entire document before starting this procedure.

Document Notes:
- Unless otherwise stated, you will have to run commands from this document as root.
- Familiarize yourself with NVIDIA developer driver installation instructions on the NVIDIA developer website before using this document.
- The supported version numbers of the installation files are listed in this document. Different versions of these tools have not been tested.

PR2 Computer Note: Only the “c1” hard drive is writeable. The two computers share a filesystem, so you will be able to use the files on “c2”. Since the GPU is installed on “c2”, you will have to build the CUDA tools on “c1” and run them on “c2”.

PR2 Starting Configuration

PR2 Computer:
- 2.6.31.10-rt-pr2 kernel (linux-image-2.6.31-10-rt_2.6.31-10.153_amd64.deb)
- Kernel headers (linux-headers-2.6.31-10-rt_2.6.31-10.153_amd64.deb)
- RT headers (linux-rt-headers-2.6.31-10_2.6.31-10.153_all.deb)
- Ubuntu 10.04 (Lucid Lynx) 64-bit

The PR2 kernel files may be already installed on your robot. If they are not, use “apt-cache search” to find and install them.

NVIDIA Drivers from the NVIDIA developer website:
- CUDA Toolkit for Ubuntu Linux 10.04 (64-bit), version 3.2.9
  - cudatoolkit_3.2.9_linux_64_ubuntu10.04.run
- GPU Computing SDK code samples, CUDA version 3.2
  - gpucomputingsdk_3.2_linux.run

Helper files from PR2 Support Website (under “Downloads”):
- cuda_toolkit.conf
- pr2_gpusdk_makefile.patch
- pr2_gpu_monitor.launch

Download the CUDA toolkit and GPU Computing SDK from the NVIDIA developer website, http://developer.nvidia.com. Copy the “cudatoolkit” and “gpucomputingsdk” files onto your robot and make them executable.

Check to make sure the NVIDIA Quadro 600 is properly installed. On c2 of the PR2, type “lspci”. You should see:

03:00.0 VGA compatible controller: nVidia Corporation Device 0df8 (rev a1)
03:00.1 Audio device: nVidia Corporation Device 0bea (rev a1)

Installing the Driver and CUDA Toolkit

Driver Installation

Run “sudo apt-get install nvidia-current” to install the NVIDIA driver. Make sure you have the driver version 260.19.06 after the installation (run “dpkg -s nvidia-current” to check version).

CUDA Toolkit

Next, install the CUDA toolkit by running the “cuda_toolkit_...” file as root from c1.

Copy the file “cudatoolkit.conf” from the PR2 Support Website to the directory “/etc/ld.so.conf.d”. Run “ldconfig” as root to set your LD_LIBRARY_PATH for the CUDA modules.

GPU SDK Installation

Finally, install the “gpu_computing...” file. Run the file to install it. Do not run the file as “root”, you can install as a regular user.

You should have a folder in your home directory called “NVIDIA_GPU_Computing_SDK”. Apply the patch “pr2_gpusdk_makefile.patch” to that directory.

~NVIDIA_GPU_Computing_SDK/ $ patch -p0 -i pr2_gpusdk_makefile.patch

In the folder “~/NVIDIA_GPU_Computing_SDK/C”, type “make” to build the CUDA code samples. Run these commands on c1.

Verify Driver Installation

Run “~/NVIDIA_GPU_Computing_SDK/C/bin/linux/release/deviceQuery” on c2. You may have to run as root. Make sure you see at least one device supporting CUDA.

Check that the GPU is functioning. Run “sudo nvidia-smi -a” to get the temperature and utilization of the GPU.

==============NVSMI LOG==============

Timestamp	: Thu Oct 21 18:53:06 2010

Driver Version	: 260.19.06

GPU 0:
Product Name	: Quadro 600
PCI Device/Vendor ID	: df810de
PCI Location ID	: 0:3:0
Display	: Connected
Temperature	: 48 C
Fan Speed	: 67%
Utilization
   GPU	: 0%
   Memory	: 3%

You can run other utilities in the “~/NVIDIA_GPU_Computing_SDK/C/bin/linux/release” directory to test GPU performance.

PR2 / ROS Integration

To monitor the GPU using the ROS diagnostics system, check out the “nvidia_gpu_monitor” package from “wg-ros-pkg”. Add the package to your ROS_PACKAGE_PATH (ex: “/opt/ros/cturtle”) and “rosmake -i” it. The “-i” option for “rosmake” marks the package as “installed”, so rosmake will not try to build it again.

Add the following to your “/etc/ros/robot.launch” file to start the GPU monitor:

<include file=”/etc/ros/cturtle/pr2_gpu_monitor.launch” />

Copy the file “pr2_gpu_monitor.launch” from the PR2 support website to the “/etc/ros/cturtle” folder.

Start the PR2 software and make sure the GPU reports “OK” in the diagnostics. The “GPU Status” will be under the “Computers” tab.

Diamondback: When using ROS Diamondback, the GPU monitor tool has moved to the “pr2_computer_monitor” package, which is installed on your PR2 by default. You can modify the file “pr2_gpu_monitor.launch” to change the package for the GPU monitor tool.