PR2 Simulator
John Hsu

---
Workshop Outline
- Simulator Overview
- Modeling PR2
- Physics Simulation
- Simulation Interfaces
- PR2 Interfaces
- Working with PR

---
Simulator Overview
- Main Software Components
  - Gazebo (ODE/Ogre)
  - ROS (as plugins in Boxturtle release)
Collision Detection
Create contact Joints
Robot Model Update
PID controllers, executives,
GUI, etc.
Physics Update
Solve constraint forces
Velocities, positions
Sensor Generation
Image, range sensors
(imu, contact...)

---
Simulator Overview
- Constrained Dynamics
  - Prismatic, revolute with explicit damping. Fixed joints.
  - Contact modeling
    - Allows interpenetration with restorative forces.
    - Decoupled x-y dry friction pyramid.
- Integrator
  - LCP formulation.
  - First order semi-implicit integrators.

---
Modeling PR2
- Δt = 1ms (matches real-time pr2_etherCAT)
- Force controlled joints
- Gravity compensation → turn gravity off
- All I/O through ROS

---
Gazebo World Configuration
<world>
 <physics:ode/>
 <rendering:gui/>
 <rendering:ogre/>
 <model:physical/>
    ...
  <model:physical/>
    ...
</world>
Integrator
Time step size
Dissipation, stabilization parameters
GUI window Properties
Ambient lighting
Sky description
Ground grid
GUI rendering update rate
Shadow technique
Physical Models
Lights, etc.

---
Sample Physics Configuration
<physics:ode>
   <stepTime>0.001</stepTime>
   <gravity>0 0 -9.8</gravity>
   <cfm>0.0000000001</cfm>
   <erp>0.2</erp>
   <quickStep>true</quickStep>
   <quickStepIters>10</quickStepIters>
   <quickStepW>1.3</quickStepW>
   <contactMaxCorrectingVel>100.0</...>
   <contactSurfaceLayer>0.001</...>
</physics:ode>

---
Example Rigid Body Model
<model:physical name=”model1” [xmlns:...]>
<body:box name="box1">
<mass>1</mass>
<ixx>1</ixx> [ixy,iyy,iyz,izz]
<geom:box name="geom1">
        <visual>
        <size>1 1 1</size>
        <material>Blue</material>
        <mesh>unit_box</mesh>
        </visual>
       </geom:box>
   </body:box>
</model:physical>

---
Gazebo Internal Data Structure
- World
  - Model
    - Body (Rigid bodies / links)
      - Inertias
      - Geom (Collision Meshes)
        - OgreVisual (Visual Meshes)
    - Joint (Constraints between rigid bodies)

---
Physics Simulation
- 3D rigid body dynamics in the inertial frame
  - f=Ma
- Constraint forces based on velocity constraints
  - Equality constraints (revolute, prismatic)
    - J1v1+J2v2=c
  - Unilateral constraints (contacts)
    - LCP formulation Jcv ≥ c.
    - Contact joints are created and destroyed at every time step.

---
Physics Simulation
- Governing Equations with velocity based LCP formulation.
- First order discretization
- Solve for constraint forces

---
Physics Simulation
- Contact Modeling
  - Gazebo friction example
    - Coulomb's friction pyramid – larger friction forces off principal friction axis.
  - Future work
    - Friction direction alignment
    - Implicit surfaces

---
Physics Simulation
- Choosing a solver
  - Pivot – Dantzig's algorithm, currently less stable, but provides “exact” solution
  - Iterative – Projected Gauss-Seidel with successive over relaxation, not “exact solution” but more stable and convergence is good in practice

---
Physics Simulation
- Solution existence and uniqueness
  - Model Stability - physically unstable models?
- Numerical stability, consistency/convergence
  - Time step size
  - Iterations per time step
  - Relaxation parameter (w)
  - Constraint “stiffness”, condition numbers, CFM, ERP (Kp,Kd) – adding to numerical stability by artificially modifying the system of equations
- Accuracy O(dt)

---
Example
Example of inner iteration convergence (rms of Δλ vs. iteration #) for 5 link pendulum.

---
Examples
- Single Pendulum Example
  - Time Step Size vs. Numerical Error
  - Inner Iterations vs. Numerical Error
  - Inner Iteration Convergence
  - Effects of CFM and ERP
- Double pendulum Example
  - Simulation vs. analytical solution

---
Pendulum without ERP
Single point mass pendulum (100kg) without error correction (ERP). Plots of hinge z-location vs. time. Effects of time step size on drift rate
10kHz Simulation
1kHz Simulation

---
Pendulum with ERP
Single point mass pendulum with error correction (ERP=0.2) at 1kHz. Plots of hinge z-location vs. time.
100kg mass
10kg mass

---
Contact Modeling
Interpenetration with fixed time stepping
Restorative force
d

---
Contact Modeling
Overshoot from collision model trying to correct interpenetration:

---
Contact Friction Modeling
- 10 Kg box on ground
  plane with 1G lateral
  acceleration.
- Dry friction coefficient
  0.9.

---
Joint Trajectory Example
Same command to the PR2 arm in simulation and on the hardware:
Simulation
PR2

---
URDF
- Description of the robot as a set of rigid linkages and joints.
- Must be a tree (single parent).

---
URDF
- Links
  - Inertial element – provides M in f=Ma.
  - Visual element – for visualization and camera sensors.
  - Collision element – enables collision detection for contact joint creation and range sensor simulation.

---
URDF
- Joints
  - Prismatic, revolute, continuous, fixed.
  - Specify joint axis for prismatic and revolute joints.
  - Dynamics – damping force is proportional to velocity.
  - Transmissions
    - Maps joint state ↔ actuator(motor) states
    - ROS package pr2_mechanism_model contains SimpleTransmission, Pr2GripperTransmission, WristTransmission.

---
PR2 Interface
- Sensor ROS topics
  - /base_scan
  - /tilt_scan
  - /narrow_stereo/*
  - /wide_stereo/*
  - /l_forearm_cam/*
  - /r_forearm_cam/*

---
Simulation vs. Real World
Real world sensor reading (left) is usually much more cluttered / noisier than simulation results (right).

---
Gazebo Plugins
- Writing you own gazebo plugins
  - Example: gazebo_plugins/src/gazebo_ros_template.cpp
    - GZREGISTER_DYNAMIC_CONTROLLER()
    - LoadChild()
    - InitChild()
    - UpdateChild()
    - FiniChild()

---
Simulation vs. Real World
- Simulation vs. real world physics
  - Contact – simulator is preset to inelastic collisions. Some contact instabilities with constraint repair approach.
  - Contact friction – friction pyramid, not accurate if resulting friction force is not aligned with the principle directions.

---
Simulation vs. Real World
- Summary cont'd:
  - Sensors – shading is interpolated across trimeshes. (Per-pixel lighting is currently experimental).
  - Joint damping – explicit, hence limited.
  - Joint Efforts / Positions – ideal motors and encoders.
  - Joint friction and efficiency not modeled.

---
Simulation Interface
- Spawn simple objects
  http://www.ros.org/wiki/simulator_gazebo/Tutorials/AddingObjectsToTheWorld
- Controlling PR2 in simulation
  https://docs.google.com/a/willowgarage.com/Doc?docid=0AXzTiNaRWL7fZGc4ZDd0N3hfMjFjZ3puZHdkYw&hl=en