Processing Camera Data
ROS + PR2 Training Workshop

---
Outline
Cameras on the PR2
The monocular image pipeline
The stereo image pipeline
Logging sensor data
Writing a vision node
[Speaker Notes: Overview of the PR2 cameras, viewing camera data and the image pipeline. Start with the cameras, what each one is good for, and how to view the image streams.]

---
Outline
Cameras on the PR2
  1. The camera suite
  1. Viewing images
  1. Adjusting camera parameters
  1. Using the texture projector
  1. Saving bandwidth
The monocular image pipeline
The stereo image pipeline
Logging sensor data
Writing a vision node
[Speaker Notes: Overview of the PR2 cameras, viewing camera data and the image pipeline. Start with the cameras, what each one is good for, and how to view the image streams.]

---
Cameras on the PR2
Wide angle color stereo
LED texture projector
Narrow angle mono stereo
5MP camera
Wide angle
 arm camera
[Speaker Notes: Just briefly introduce each camera.]

---
Viewing Images
rviz node
  - Displays panel → Add → Camera
image_view node
  - $ rosrun image_view image_view image:=<camera>/<image>
www.ros.org/wiki/rviz/DisplayTypes/Camera
www.ros.org/wiki/image_view
[Speaker Notes: Display the data from each camera. Try each of the two methods. Show the processed data. Describe each camera while displaying the data. Wide angle color stereo. FOV??? 30 fps. Useful if you need a wide view, with color. Not good for detail. Perhaps blob tracking. Narrow angle monochrome stereo. FOV??? 30fps. Much narrower view + monochrome means more resolution. Very narrow, so need to know where to point it. Texture projector. (Introduce dynamic_reconfigure here???) Synced with narrow stereo. Doesn't interfere with the wide stereo. Focused 1-2m from the robot. Much better stereo info. Tabletop manipulation, floor plane detection. Eye safe, but annoying (working on moving it out of the visible spectrum.) Arm cam. Same as wide cam. See what the robot is holding, or get weird views. 5mp color camera. FOV??? Frame rate???]

---
Configuring Your Cameras
$ rosrun dynamic_reconfigure reconfigure_gui
For cameras:
Adjust camera parameters (exposure, gain, ...)
Turn texture projector on/off
Adjust stereo processing parameters
www.ros.org/wiki/dynamic_reconfigure

---
Adjust Camera Parameters
Cameras:
/l_forearm_cam
/r_forearm_cam
/wide_stereo_both
/narrow_stereo_both
/prosilica_driver
For stereo cameras, “both” propagates settings to left & right

---
Using the Texture Projector
projector_mode – whether projector is turned on
*_trig_mode – whether the camera syncs with the projector on all, no, or some frames
Camera namespaces change when using the texture projector:
  1. /narrow_stereo
  1. /narrow_stereo_textured

---
Saving Bandwidth
Each image topic has alternate compressed versions
Transports available out of the box
  1. “raw” - default, uncompressed
  1. “compressed” - JPEG or PNG
  1. “theora” - Theora video codec
With image_view:
$ rosrun image_view image_view image:=<camera>/<image> compressed
www.ros.org/wiki/image_transport

---
Outline
Cameras on the PR2
The monocular image pipeline
  1. Camera calibration
  1. Basic processing
    1. De-Bayering
    1. Rectification
The stereo image pipeline
Logging sensor data
Writing a vision node
[Speaker Notes: The images I showed had a lot of processing performed on them. The raw images out of the cameras don't quite look that good. For example, (show the wide images raw and image_rect_color), here are the wide camera images raw, and after processing. The stuff that gets images from their raw state into a state that's good to work with is called the image_pipeline. I'll start by describing the monocular image pipeline.]

---
The Monocular Image Pipeline
image_view
rviz
Images
Settings
Camera
Driver
image_proc
Your vision
node
<camera>/image_raw
<camera>/image_rect_color
<camera>/camera_info
www.ros.org/wiki/camera_drivers, www.ros.org/wiki/image_pipeline
[Speaker Notes: Each camera talks to a camera driver. The camera sends images and their parameters to the driver, and the driver can change parameters in the camera. Parameters are things like exposure, but also things like lens distortion. The camera driver publishes the raw images from the camera on the ROS topic <camera>/image_raw, and all of the necessary parameters on the topic <camera>/camera_info. The messages sent out on these two topics will have the same timestamp, so we can synchronize them later. The image_proc node is responsible for processing the raw images and making them presentable. It debayers the images to produce color, and undistorts them so that lines are straight. It then publishes the processed images on a corresponding topic like <camera>/image_rect_color. They also have the same timestamp as the original image, so it's easy to synchronize them. The images are now ready to work with. Your node should take in a synchronized processed image and camera_info message.]

---
Mono Camera Calibration
After
Before
Distortion
Parameters → camera driver
CameraInfo message published with each Image
www.ros.org/wiki/camera_calibration
[Speaker Notes: I mentioned that image_proc undistorts images so that lines are straight and corners are corners. It gets the parameters it needs from the camera_info message, which gets populated by the camera driver. But how does the camera know what distortion is in it's lenses? The factory can partially guess, but really you need to do camera calibration to discover these distortion parameters and store them in the camera for future use.]

---
Mono Camera Calibration
Get a large checkerboard
$ rosrun camera_calibration cameracalibrator.py --size 7x6
--square 0.108 image:=/<camera>/image_raw camera:=/<camera>
www.ros.org/wiki/camera_calibration/Tutorials/MonocularCalibration
www.ros.org/wiki/camera_calibration
[Speaker Notes: Luckily there's a simple tool you can use to do calibration with the help of a large checkerboard. I won't go through more details now, there's a great tutorial on the wiki page listed and calibrating your cameras will actually be your first exercise in a minute. (Note: second camera argument for service call. set_camera_info. Repeated for max flexibility.)]

---
Mono Processing
image_proc publishes image topics that are
  - De-bayered (grayscale or color)
  - Rectified
  - On topics:
  - <camera>/image_mono
  - <camera>/image_color
  - <camera>/image_rect
<camera>/image_rect_color
www.ros.org/wiki/image_proc
[Speaker Notes: Stereo processing produces 3D data that can be viewed in two different ways. The first is a disparity image, which is published on the topic <stereo_camera>/disparity (with the same timestamp as the original image). The second is a 3D point cloud, which is published on the points topic.]

---
Outline
Cameras on the PR2
The monocular image pipeline
The stereo image pipeline
  - Stereo calibration
  1. Stereo processing (3D)
  1. Viewing disparity images and point clouds
  1. Adjusting stereo parameters
Logging sensor data
Writing a vision node
[Speaker Notes: So far everything that I've been describing is for monocular processing. But we have stereo cameras on the robot that can produce 3D data and it's time to use them. First I'll show you the kind of 3D data that the stereo cameras can produce and how to view it. Then, as in the monocular pipeline, we'll discuss a little about calibration. Finally, I'll leave you with an exercise to calibrate your stereo cameras.]

---
The Stereo Image Pipeline
image_view
rviz
Images
Settings
Images
Settings
Camera
Driver
Camera
Driver
stereo_image_proc
Your vision
node
<camera>/left/image_rect_color
<camera>/right/image_rect_color
<camera>/disparity
<camera>/points
<camera>/left/image_raw
<camera>/left/image_raw
<camera>/left/camera_info
<camera>/left/camera_info
www.ros.org/wiki/camera_drivers, www.ros.org/wiki/image_pipeline
[Speaker Notes: The stereo image pipeline is a lot like the monocular image pipeline, with a few exceptions shown here in red. First, there are 2 cameras, a left and a right camera, each with a driver producing raw images and camera info. We use stereo_image_proc instead of image_proc And get undistorted left AND right images, as well as a disparity image and a point cloud.]

---
Stereo Camera Calibration
After
Before
Distortion
Stereo rectification
3D geometry
Parameters → camera drivers
CameraInfo message published with each Image
www.ros.org/wiki/camera_calibration
[Speaker Notes: Just like in the monocular pipeline, in order to undistort our images we need to perform camera calibration. Stereo calibration does more, however. It also maps points between the two cameras. Then we can rectify the images, creating image planes that are in the same plane. In rectified images, a single point in space lies on the same horizontal line in each image. Calibration also figures out the 3D geometry of the cameras, so that we can project points into the 3D world.]

---
Stereo Processing
stereo_image_proc publishes
  - Disparity images
  - Point clouds
  - On topics:
  - <stereo_camera>/disparity
  - <stereo_camera>/points
www.ros.org/wiki/stereo_image_proc
[Speaker Notes: Stereo processing produces 3D data that can be viewed in two different ways. The first is a disparity image, which is published on the topic <stereo_camera>/disparity (with the same timestamp as the original image). The second is a 3D point cloud, which is published on the points topic.]

---
Viewing Disparity Images
$ rosrun image_view stereo_view
stereo:=narrow_stereo image:=image_rect
pright
pleft
d
p
pright
pleft
d
[Speaker Notes: The stereo algorithm gives you disparity, how far apart the same point is in the left and right images. The disparity image you see here is in color-coded. The point p in the disparity image is p_left in the left image and p_right in the right image. The distance d is the disparity. You can view the left and right images as well as the false-color disparity image using the stereo_view version of image_view.]

---
Viewing Point Clouds
Displays panel → Add → Point Cloud
Enter the topic in the red box
[Speaker Notes: Of course, if we know which points match in the two images, we can triangulate to get the point in 3D. If we do this to every point in the image (that has disparity information) we get a point cloud, a set of 3D points. To view the point cloud, use rviz and add a point cloud display panel, connected to the topic <stereo_camera>/points.]

---
Adjust Stereo Parameters
In reconfigure_gui, look for
<stereo>/stereo_image_proc
www.ros.org/wiki/stereo_image_proc/Tutorials/ChoosingGoodStereoParameters

---
Exercise #1
Calibrate your narrow stereo cameras.
www.ros.org/wiki/camera_calibration/Tutorials/
StereoCalibration
But do not “Commit” to the camera, or you will have to run full-body calibration again!
[Speaker Notes: Follow the tutorial online to calibrate the narrow stereo cameras on your robot.]

---
Outline
Cameras on the PR2
The monocular image pipeline
The stereo image pipeline
Logging sensor data
  - Recording and playback
  - Visual inspection with rxbag
  - Bags and ROS time
Writing a vision node
[Speaker Notes: So now that we've gone over the entire image pipeline, it's time for an exercise.]

---
Logging Sensor Data
Recording data:
  - $ rosbag record r_forearm_cam/image_raw r_forearm_cam/camera_info tf
Play back data:
  - $ rosbag play XXX.bag
What's in a bag file:
  - $ rosbag info mystery_data.bag
www.ros.org/wiki/rosbag/Tutorials/Recording and playing back data

---
Visual Inspection with rxbag
$ rxbag XXX.bag
View thumbnails:
Right-click → Thumbnails...
→ select topic(s)
Image viewer for a topic:
Right-click
→ View (by datatype)... → sensor_msgs/Image
→ <topic> → Image
www.ros.org/wiki/rxbag
Playback
Click to jump

---
Bags and ROS Time
Do not play back a bag against a live robot!
Recorded message timestamps will be far in the past relative to “wall-clock” time
When using time-aware nodes with bagged data:
  1. $ rosbag play --clock XXX.bag
  1. Set parameter /use_sim_time = True before starting nodes
Do not set /use_sim_time on a live robot!
www.ros.org/wiki/Clock

---
Outline
Cameras on the PR2
The monocular image pipeline
The stereo image pipeline
Logging sensor data
Writing a vision node
  - Subscribing to camera topics
  - Interfacing with OpenCV
  - Publishing images
[Speaker Notes: So now that we've gone over the entire image pipeline, it's time for an exercise.]

---
Processing Images in ROS
<camera>/image_rect
<camera>/camera_info
Your Node
OpenCV image (cv_bridge)
OpenCV camera info (image_geometry)
Solve vision
Publish results
www.ros.org/wiki/cv_bridge
www.ros.org/wiki/image_geometry

---
Subscribing to Camera Topics
Use image_transport instead of ros::Subscriber
  - Compression (JPEG/PNG, Theora)
  - Add others as plugins
Subscribe to image AND camera_info topics
  - Synchronized time stamps
  - CameraSubscriber handles the synchro
www.ros.org/wiki/image_transport

---
Subscribing to Camera Topics
1 #include <ros/ros.h>
2 #include <image_transport/image_transport.h>
3
4 class MyVisionNode
5 {
6 ros::NodeHandle nh_;
7 image_transport::ImageTransport it_;
8 image_transport::CameraSubscriber sub_;
9
10 public:
11 MyVisionNode()
12 : it_(nh_)
13 {
14 sub_ = it_.subscribeCamera("image_topic", 1, &MyVisionNode::imageCb, this);
15 }
16
17 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
18 const sensor_msgs::CameraInfoConstPtr& info_msg)
19 {
20 // ...
21 }
22 };

---
Subscribing to Camera Topics
1 #include <ros/ros.h>
2 #include <image_transport/image_transport.h>
3
4 class MyVisionNode
5 {
6 ros::NodeHandle nh_;
7 image_transport::ImageTransport it_;
8 image_transport::CameraSubscriber sub_;
9
10 public:
11 MyVisionNode()
12 : it_(nh_)
13 {
14 sub_ = it_.subscribeCamera("image_topic", 1, &MyVisionNode::imageCb, this);
15 }
16
17 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
18 const sensor_msgs::CameraInfoConstPtr& info_msg)
19 {
20 // ...
21 }
22 };

---
Subscribing to Camera Topics
1 #include <ros/ros.h>
2 #include <image_transport/image_transport.h>
3
4 class MyVisionNode
5 {
6 ros::NodeHandle nh_;
7 image_transport::ImageTransport it_;
8 image_transport::CameraSubscriber sub_;
9
10 public:
11 MyVisionNode()
12 : it_(nh_)
13 {
14 sub_ = it_.subscribeCamera("image_topic", 1, &MyVisionNode::imageCb, this);
15 }
16
17 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
18 const sensor_msgs::CameraInfoConstPtr& info_msg)
19 {
20 // ...
21 }
22 };

---
Subscribing to Camera Topics
1 #include <ros/ros.h>
2 #include <image_transport/image_transport.h>
3
4 class MyVisionNode
5 {
6 ros::NodeHandle nh_;
7 image_transport::ImageTransport it_;
8 image_transport::CameraSubscriber sub_;
9
10 public:
11 MyVisionNode()
12 : it_(nh_)
13 {
14 sub_ = it_.subscribeCamera("image_topic", 1, &MyVisionNode::imageCb, this);
15 }
16
17 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
18 const sensor_msgs::CameraInfoConstPtr& info_msg)
19 {
20 // ...
21 }
22 };

---
Subscribing to Camera Topics
1 #include <ros/ros.h>
2 #include <image_transport/image_transport.h>
3
4 class MyVisionNode
5 {
6 ros::NodeHandle nh_;
7 image_transport::ImageTransport it_;
8 image_transport::CameraSubscriber sub_;
9
10 public:
11 MyVisionNode()
12 : it_(nh_)
13 {
14 sub_ = it_.subscribeCamera("image_topic", 1, &MyVisionNode::imageCb, this);
15 }
16
17 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
18 const sensor_msgs::CameraInfoConstPtr& info_msg)
19 {
20 // ...
21 }
22 };

---
Open Computer Vision Library
opencv.willowgarage.com

---
Using ROS messages with OpenCV
cv_bridge
ROS sensor_msgs/Image → OpenCV IplImage
image_geometry
ROS sensor_msgs/CameraInfo → OpenCV calibration matrices
  - Many useful functions in the camera model classes
www.ros.org/wiki/cv_bridge/Tutorials
www.ros.org/wiki/image_geometry

---
ROS Image -> OpenCV
1 #include <cv_bridge/CvBridge.h>
2
3 class MyVisionNode
4 {
5 sensor_msgs::CvBridge bridge_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 IplImage *cv_image = NULL;
12 try {
13 cv_image = bridge_.imgMsgToCv(image_msg, "bgr8");
14 }
15 catch (sensor_msgs::CvBridgeException& error) {
16 ROS_ERROR("Couldn't convert image with encoding %s",
17 image_msg->encoding.c_str());
18 return;
19 }
20 }
21 };

---
ROS Image -> OpenCV
1 #include <cv_bridge/CvBridge.h>
2
3 class MyVisionNode
4 {
5 sensor_msgs::CvBridge bridge_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 IplImage *cv_image = NULL;
12 try {
13 cv_image = bridge_.imgMsgToCv(image_msg, "bgr8");
14 }
15 catch (sensor_msgs::CvBridgeException& error) {
16 ROS_ERROR("Couldn't convert image with encoding %s",
17 image_msg->encoding.c_str());
18 return;
19 }
20 }
21 };

---
ROS Image -> OpenCV
1 #include <cv_bridge/CvBridge.h>
2
3 class MyVisionNode
4 {
5 sensor_msgs::CvBridge bridge_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 IplImage *cv_image = NULL;
12 try {
13 cv_image = bridge_.imgMsgToCv(image_msg, "bgr8");
14 }
15 catch (sensor_msgs::CvBridgeException& error) {
16 ROS_ERROR("Couldn't convert image with encoding %s",
17 image_msg->encoding.c_str());
18 return;
19 }
20 }
21 };

---
ROS Image -> OpenCV
1 #include <cv_bridge/CvBridge.h>
2
3 class MyVisionNode
4 {
5 sensor_msgs::CvBridge bridge_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 IplImage *cv_image = NULL;
12 try {
13 cv_image = bridge_.imgMsgToCv(image_msg, "bgr8");
14 }
15 catch (sensor_msgs::CvBridgeException& error) {
16 ROS_ERROR("Couldn't convert image with encoding %s",
17 image_msg->encoding.c_str());
18 return;
19 }
20 }
21 };

---
ROS CameraInfo -> OpenCV
1 #include <image_geometry/pinhole_camera_model.h>
2
3 class MyVisionNode
4 {
5 image_geometry::PinholeCameraModel cam_model_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 cam_model_.fromCameraInfo(info_msg);
12 }
13 };

---
ROS CameraInfo -> OpenCV
1 #include <image_geometry/pinhole_camera_model.h>
2
3 class MyVisionNode
4 {
5 image_geometry::PinholeCameraModel cam_model_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 cam_model_.fromCameraInfo(info_msg);
12 }
13 };

---
ROS CameraInfo -> OpenCV
1 #include <image_geometry/pinhole_camera_model.h>
2
3 class MyVisionNode
4 {
5 image_geometry::PinholeCameraModel cam_model_;
6
7 public:
8 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
9 const sensor_msgs::CameraInfoConstPtr& info_msg)
10 {
11 cam_model_.fromCameraInfo(info_msg);
12 }
13 };

---
Publishing Image Topics
1 class MyVisionNode
2 {
3 ros::NodeHandle nh_;
4 image_transport::ImageTransport it_;
5 image_transport::Publisher pub_;
6
7 public:
8 MyVisionNode()
9 : it_(nh_)
10 {
11 pub_ = it_.advertise("image_out", 1);
12 }
13
14 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
15 const sensor_msgs::CameraInfoConstPtr& info_msg)
16 {
17 // ...
18 pub_.publish(bridge_.cvToImgMsg(image, "bgr8"));
19 }
20 };

---
Publishing Image Topics
1 class MyVisionNode
2 {
3 ros::NodeHandle nh_;
4 image_transport::ImageTransport it_;
5 image_transport::Publisher pub_;
6
7 public:
8 MyVisionNode()
9 : it_(nh_)
10 {
11 pub_ = it_.advertise("image_out", 1);
12 }
13
14 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
15 const sensor_msgs::CameraInfoConstPtr& info_msg)
16 {
17 // ...
18 pub_.publish(bridge_.cvToImgMsg(image, "bgr8"));
19 }
20 };

---
Publishing Image Topics
1 class MyVisionNode
2 {
3 ros::NodeHandle nh_;
4 image_transport::ImageTransport it_;
5 image_transport::Publisher pub_;
6
7 public:
8 MyVisionNode()
9 : it_(nh_)
10 {
11 pub_ = it_.advertise("image_out", 1);
12 }
13
14 void imageCb(const sensor_msgs::ImageConstPtr& image_msg,
15 const sensor_msgs::CameraInfoConstPtr& info_msg)
16 {
17 // ...
18 pub_.publish(bridge_.cvToImgMsg(image, "bgr8"));
19 }
20 };

---
Outline
Cameras on the PR2
The monocular image pipeline
The stereo image pipeline
Logging sensor data
Writing a vision node
[Speaker Notes: Overview of the PR2 cameras, viewing camera data and the image pipeline. Start with the cameras, what each one is good for, and how to view the image streams.]

---
Exercise #2
Draw the location of the robot gripper (according to tf) on an image stream.
http://www.ros.org/wiki/image_geometry/Tutorials/ProjectTfFrameToImage
The tutorial uses a bag as the data source, so remember:
Do not play back a bag against a live robot!
Do not set /use_sim_time on a live robot!

---
Questions?
http://www.ros.org/
http://opencv.willowgarage.com/
ros-users@code.ros.org

---
Cameras on the PR2

---
Viewing Images (image_view)
$ rosrun image_view image_view
image:=r_forearm_cam/image_raw
www.ros.org/wiki/image_view

---
The Image Pipeline
image_view
stereo_view
rviz
Camera calibration
image_proc/
stereo_image_proc
Your vision processing nodes!
Camera driver
www.ros.org/wiki/image_pipeline

---
Camera Drivers
Image stream
Camera settings (exposure, gain, etc.)
Camera
Driver
<camera>/image_raw
<camera>/camera_info
www.ros.org/wiki/camera_drivers

---
Camera Calibration
Calibration characterizes:
  - Distortion
  - How 3D points project to the image plane
  - How to rectify stereo pairs
Parameters normally stored by the camera driver
Published in a CameraInfo message with each Image
www.ros.org/wiki/camera_calibration

---
Camera Drivers
Stream sensor images and publish them to ROS topics
Configure camera settings (exposure, gain, etc.)
Output topics:
  - <camera>/image_raw – the raw image data (often Bayer)
  - <camera>/camera_info – camera metadata, including calibration parameters
www.ros.org/wiki/camera_drivers

---
Camera Drivers
Image stream
Camera settings (exposure, gain, etc.)
Camera
Driver
<camera>/image_raw
<camera>/camera_info
www.ros.org/wiki/camera_drivers

---
The Image Pipeline
image_view
stereo_view
rviz
Camera calibration
image_proc/
stereo_image_proc
Your vision processing nodes!
Camera driver
www.ros.org/wiki/image_pipeline

---
Debayering and Rectification
Basic operations performed by
  - image_proc (monocular cameras)
  - stereo_image_proc (stereo cameras)

---
Processing Images in ROS
Typical vision node workflow:
  - Subscribe to the camera topics
  - Image & CameraInfo messages → OpenCV types
  - Solve vision!
  - Publish poses, output images, etc.

---
Outline
Cameras on the PR2
Viewing images
The monocular image pipeline
  1. Raw images & the camera driver
    1. Adjusting image params
  1. De-Bayering & rectification
    1. Camera calibration
    1. image_proc node
The stereo image pipeline
  1. Viewing disparity images and point clouds
  - stereo_image_proc node
  1. More calibration
[Speaker Notes: Overview of the PR2 cameras, viewing camera data and the image pipeline. Start with the cameras, what each one is good for, and how to view the image streams.]