Toolkit Doc23 Spine E-chain
Sept20, 2010

---
Spine E-chain Cable Install
- Make sure the Robot is turned off and unplugged from wall power.
- Remove the Rear Bottom Panel. (Doc2)
- Remove the Rear Bellows. (Doc9)
- Using the 3mm bit together with the T-handle driver, remove the 2 locking screws at the top of the E-chain and 2 at the bottom. (Fig. 1,2)
- At the top of the E-chain, try to slide the E-chain out and if necessary using a 7mm open end wrench (not provided) loosen the 2 7mm Nyloc nuts to allow the bracket with E-chain to slide out. Do this for the other end, first sliding the Cable Channel Cover up out of the way. (Fig. 3,4)
Fig 3
Fig 4
Fig 1
Cover
Fig 2

---
- Starting at the top, carefully snap out the outside E-chain links. They are linked together but can come apart if you are not careful. (Fig. 5)
- There are 3 levels of channels. It is recommended to run any additional cables on the outside channel. (Fig. 6)
- After you are done running cables, carefully snap the E-chain links back in place one at a time. (Fig. 5)
- Slide the E-chain back into place and using Loctite 248, install the 4 screws and torque to 1.36Nm.
- If necessary tighten the 4 Nyloc nuts until the washers are not loose.
- After you are done running cables, carefully snap the E-chain links back in place one at a time. (Fig. 7)
- Slide the E-chain back into place and using Loctite 248, install the 4 screws and torque to 1.36Nm.
- If necessary tighten the 4 nyloc nuts until the washers are not loose.
- Reinstall the Rear Bellows
- Reinstall the Rear Bottom Panel
Fig 7
Fig 5
Fig 6