Installing Your Basestation
ROS + PR2 Training Workshop

---
Introduction
Why do we use a basestation?
  1. Seamless transition between wired and wireless networking
  2. Servicing the PR2
  3. Intermediate storage for HW logs

---
PR2 and Basestation Network

---
Network Requirements
Basestation needs static IP
  1. Either assign directly or DHCP server must assign consistently
On VPN port (default: 1194) basestation must be visible both wired and wirelessly at same IP address

---
Basestation Setup: physical

---
Basestation Setup: computer
Default hostname is “basestation.”
To change name you must edit:
  1. /etc/hostname
  2. /etc/hosts
  3. /etc/dhcp3/dhclient.conf (Only if using DHCP)
To set static IP, edit:
  1. /etc/network/interfaces
  2. /etc/resolv.conf
If you use DHCP:
  1. DHCP server MUST assign consistent IP address via client-id
To configure the basestation VPN certificate, run:
  1. sudo /etc/openvpn/gen_server_key

---
Configuring the Robot
To use the basestation to configure a robot, plug it into the robot service port.

---
Configuring Robot Wireless
1. The robot comes equipped with a Linksys WRT610n router running ddwrt
2. To configure it, plug the basestation into the robot service port
3. Use firefox to go to: http://10.68.0.5
4. The router must stay at that address, but other settings can be changed as necessary to connect to your wireless

---
Pairing a Robot
Pairing a robot with a basestation is a mostly automated with the “robot-brand” command:
$ sudo robot-brand <ROBOT-NAME> <C1-NAME> <C2-NAME> <SUBNET> [<IP>]
$ sudo robot-brand green green1 green2 10.68.1.0
$ sudo robot-brand green green1 green2 10.68.1.0 192.168.1.100
  1. c1 and c2 will end up named green1 and green2, but the c1 and c2 hostnames will continue to work internally.
  2. <SUBNET> is the vpn subnet to use, this can almost always be 10.68.1.0 unless you are using multiple robots with the same basestation
  3. <IP> is the static IP of your basestation

---
Pairing a robot: forwarding
1. It is convenient (but not necessary) to set up the basestation to forward a specific IP address to the robot computers.
2. Edit the file: /etc/robot-forward.conf:
   <C1-NAME> 10.68.1.1 <ROBOT-IP1>
   <C2-NAME> 10.68.1.2 <ROBOT-IP2>
   green1 10.68.1.1 192.168.1.101 # Static IP setup
   green2 10.68.1.2 192.168.1.102 # Static IP setup
   red1 10.68.1.1 dhcp # dhcp setup
   red2 10.68.1.2 dhcp # dhcp setup
3. NOTE: if using dhcp, the dhcp-server must respect the client-id field and will use the name of the computer as the client-id.
4. To turn on forwarding run:
   $sudo robot-forward start

---
Generating User VPN Keys
1. If you don't want to forward traffic to the robot, you will need to allow users onto the robot VPN network
2. Run:
   $sudo /etc/openvpn/gen_user_key <NAME>
3. This will create a file: /etc/openvpn/<NAME>.tgz
4. If a user has openvpn set up on their computer, they should be able to untar this file in their openvpn directory and start openvpn

---
Debugging Network Problems
<Will fill in this section as we practice setting up basestations/robots and run into problems>

---
Using the KVM
1. Plug the basestation into the robot service port
2. To to: http://10.68.0.91 (or http://10.68.0.92)
3. Choose “Advance Console” and click Launch
4. Let it run “JavaRSM.jnlp”
5. Click the + and login to:
  1. 10.68.0.91, root, changeme
  2. 10.68.0.92, root, changeme
1. Click on the “Remote KVM Console” Tab
2. Click on one of the servers to connect to

---
Bagfile Upload Policy
1. Once per day, a cron-job on the basestation will pull the contents from the robot: “/hwlog” directory via rsync
2. It will then attempt to send these log-files back to WG for processing
3. If your basestation does not have network access, you will be responsible for doing this step manually.
  1. Copy the scripts in: /home/prdata/hwlog-scripts to a machine with internet access
  2. Copy all of the bagfiles to a machine with internet access
  3. Run send.py:
     $sudo ./send.py <ROBOT_ID> /path/to/bagfiles

---
Where To Get More Help
1. Everything covered here should be mentioned in the PR2 Manual
2. The PR2-documentation website contains additional FAQ information
3. Mailing list:
  1. pr2-admin@lists.willowgarage.com

---
Practice

---
Set up your own basestation
1. Get a copy of the handout with names and IP addresses to use
2. Change the basestation name to...
3. Change the basestation IP to...
4. Configure your robot's wireless to connect to the “willow_demo” network
5. Pair it with your robot and give your robot a new name...
6. Set up forwarding to your robot from new IPs
7. Make sure that it's working over both wired and wireless links