Toolkit Doc4 WAN Port RJ45
April 26, 2010

---
Wide Area Network Conector Repair (1)
Panel Mount RJ45, Removal - 1205
  - Using the 2mm bit with the T-handle driver, remove the 2 screws. 3054-10 (Fig 1)
  - Using the needle nose pliers or any reasonable means, extract the RJ45 connector from within the robot. (Fig 2)
  - Undo the latch and remove the RJ45 connector.
    (Fig 3,4)
RJ45, Install
  - Snap the RJ45 connnector into the panel mounting flange (Fig 5)
  - Make sure that the RJ45 is fully seated in the flange. It will only mount in one direction. (Fig 6)
  - Verify that the retaining spring arm is fully seated in its slot by inserting the 1.5mm bit as shown. (Fig 7)
Fig 5
Fig 1
Fig 6
Fig 2
Fig 7
Fig 4
Fig 3

---
Wide Area Network Conector Repair (2)
  - Verify that the retaining spring arm is not damaged and is latching the RJ45 securly by gently tugging on the RJ45. It should not pull out. (Fig 8)
  - Snap the cable back into the RJ45 connector.
    (Fig 9)
  - Do not use Loctite. Torque the screws to 0.68Nm using the Small torque driver. Connector snap should be up. (Fig 10)
Fig 8
Fig 9
Fig 10