Toolkit Doc6 Top Front/Rear Panels
April 28, 2010

---
Top Front Panel R/R
Top Front Panel, Removal - 2180
  - Using the 4mm bit with the T-handle driver, remove the 2 screws one on each side. 3063-14 (Fig 1)
  - Using the Needle Nose pliers or a small Flathead screwdriver, about 4cm from the bottom, gently pry the Collar forward until the snap releases. Do this on both sides. (Fig 2,3)
  - Slide the Panel out by pulling straight forward. You may have to lift it slightly to clear a bolt on the right side. (Fig 4)
Top Front Panel, Install
  - Reverse the removal procedure.
  - Push the bottom of the Panel on both sides until the snaps engage.
  - Using Loctite 248, install the 2 Flathead screws and torque to 1.58Nm using the Large torque driver.
Fig 4
Fig 1
Fig 3
Fig 2

---
Rear Top Panel R/R
Rear Top Panel, Removal - 2175
  - Using the 5mm bit with the T-handle driver, remove the 2 screws one on each side. 3063-14 (Fig 1)
  - Pulling firmly on the bottom edge or sides of the Panel, release the 2 snaps. (Fig 3)
  - While gently lifting the right side, pull straight back slowly rock the Panel off being aware that it is a tight fit under the Head Pan Rear Panel. (Fig 4)
Rear Top Panel, Install
  - Using Loctite 248, install the 2 Flathead screws and torque to 1.58Nm using the Large torque driver.